## Slide 1: Cathkin estates Tractor Expenditure root cause analysis
23rd June 2026

## Slide 2: Tractor expenditure: actual vs. industry standard
Chart: Year of Service
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 500 hrs | 1000 hrs | 1500 hrs | 2000 hrs | 2500 hrs | 3000 hrs | 3500 hrs | 4000 hrs | 4500 hrs | 5000 hrs | 5500 hrs | 6000 hrs | 6500 hrs | 7000 hrs | 7500 hrs | 8000 hrs | 8500 hrs | 9000 hrs | 9500 hrs | 10000 hrs
Expected (Annual) | 525 | 1575 | 2625 | 3675 | 4725 | 5775 | 6825 | 7875 | 8925 | 9975 | 11025 | 12075 | 13125 | 14175 | 15225 | 16275 | 17325 | 18375 | 19425 | 20475
Actual | 22316.61 | 18388.69 | 67096.97 | 59542.93 | 203147.93 | 117424.37
Expected,Cummulative | 525 | 2100 | 4725 | 8400 | 13125 | 18900 | 25725 | 33600 | 42525 | 52500 | 63525 | 75600 | 88725 | 102900 | 118125 | 134400 | 151725 | 170100 | 189525 | 210000
Actual, Cummulative | 525 | 2100 | 4725 | 8400 | 13125 | 35441.61 | 53830.3 | 120927.27 | 180470.2 | 383618.13 | 501042.5
Modelled based on 500 hrs per year
Cumulative expenditure: ZAR 500k
Expected expenditure: ZAR 65k
Actual expenditure is over 7 times greater than industry standard

## Slide 3: Tractor expenditure: actual vs. industry standard
Chart: Year of Service
| 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 500 hrs | 1000 hrs | 1500 hrs | 2000 hrs | 2500 hrs | 3000 hrs | 3500 hrs | 4000 hrs | 4500 hrs | 5000 hrs | 5500 hrs | 6000 hrs | 6500 hrs | 7000 hrs | 7500 hrs | 8000 hrs | 8500 hrs | 9000 hrs | 9500 hrs | 10000 hrs
Expected (Annual) | 525 | 1575 | 2625 | 3675 | 4725 | 5775 | 6825 | 7875 | 8925 | 9975 | 11025 | 12075 | 13125 | 14175 | 15225 | 16275 | 17325 | 18375 | 19425 | 20475
Actual | 22316.61 | 18388.69 | 67096.97 | 59542.93 | 203147.93 | 117424.37
Expected,Cummulative | 525 | 2100 | 4725 | 8400 | 13125 | 18900 | 25725 | 33600 | 42525 | 52500 | 63525 | 75600 | 88725 | 102900 | 118125 | 134400 | 151725 | 170100 | 189525 | 210000
Actual, Cummulative | 525 | 2100 | 4725 | 8400 | 13125 | 35441.61 | 53830.3 | 120927.27 | 180470.2 | 383618.13 | 501042.5
Modelled based on 500 hrs per year
2021: 967 hrs/2133 hrs
1000 hr service
Powertrain Split & Diff Rebuild
2022: Hours Not Listed/2133 hrs (?)
Rear Hydraulic Lift Arm Repair
Stud Repair & Filter Service
Starter Diagnosis
2024: Hours Not Listed
Drivetrain Overhaul: new flywheel assembly, new double clutch kit with clutch discs, renewing rear main oil seals, replacing release bearing assembly
2023: Hours Not Listed
Starter Motor Replacement (6k)
Clutch Overhaul (54k)
2025: Hours Not Listed/4316 hrs
Cylinder Head Rebuild & Top-End, Scheduled filters and fuel service (114k)
Non-Start Wiring Harness Repair
Double Clutch & Crank Seal (56k)
Slasher Gearbox (26k)
2026: Hours Not Listed/2236/1937 hrs
Repairs (awaiting invoice, 21k)
Various: Water Pipe & 4x4 Sensor, PTO Shaft & Joint Assembly, Gear Lever Replacement & Linkage (11k)
New Starter (26k)
Rear Lift Arm & Bushing Rebuild (26k)
Seal Split Repair & Orbital Overhaul (20k)

## Slide 4: Root cause analysis
Conclusion | Financial & Invoice Evidence | Engineering & Topographical Root Cause | Tactical Management Action
Severe Operator Overloading or "Clutch Riding” | 4 Clutch overhauls/flywheel skims (2021–2026). Multiple Rear Main Crankshaft Oil Seal kits. | Operator Error + Steep Slopes: Drivers ride clutch. Steep firebreaks pool engine oil against rear main seal. Friction heat degrades seal, coating plates in oil | Enforce Low Range (Gears L1–L3). Mandatory driver gear training. Consider moving to Power Shuttle/Hydrostatic tractor
Lack of thorough Daily Inspections & Terrain Impact | Destroyed cylinder head 8 Skid runner replacements. Slasher Gearbox failure. | Missed Warnings + Shock Loads: Daily leaks un-noticed. Slasher bottoms out on undulating turf. Ground-striking forces travel up PTO shaft, shattering gearbox gears. | Implement daily pre-start sign-off sheet. Weekly clutch housing weep-hole audit. Retrofit trailing caster wheels to lift skids 2–3 cm.
Absence of an Economic Limit of Repair Policy | ZAR 500k spent on a tractor worth ZAR 200k Invoices treated as isolated costs | Policy Deficit: Absence of a formalised asset retention framework or cumulative lifecycle expenditure tracker. | Implement the Industry Rule: Red-flag single repairs >30% market value. Dispose/trade-in if 24-month spend >50% value.
Executive summary

## Slide 5: Severe Operator Overloading or "Clutch Riding”
Evidence and Impact:
  Invoice History: Repetitive, abnormal cycle of clutch overhauls, flywheel skimming, replacement flywheels, and sheared gear linkages/shattered gear levers across 2021, 2023, 2024, and 2026 (Invoices: INJ42940, INC00243, 104406, 67045, 88520).
  Physical Degradation: Systemic failure of the Rear Main Crankshaft Oil Seal / Housing Kits (replaced/quoted April-23, Feb-24, Oct-25, Feb-26).
Likely Root Cause:
    Operational Misuse: Operators "ride" the clutch pedal to modulate speed instead of choosing a lower gear range and using the throttle.
    Absence of Active Field Policing: Manager/Supervisors failed to monitor, audit, and correct operator behaviours.
    Thermal & Topographical Stress: Forcing the tractor up steep terrain in high gear creates extreme friction heat warping flywheels and destroying adjacent rubber crankshaft oil seals. Engine oil migrates onto the clutch plates, causing permanent slippage and accelerating drivetrain burnout.
Mandatory Training: Enforce a strict "foot off the clutch pedal" rule with signed annual driver training records.
Supervisory Field Mandate: Integrate active machine operation monitoring into supervisor field routines, forcing immediate lockout and machine retraining for any operator caught riding a pedal.
Gear Selection Mandate: Require all ground-engaging slasher work and firebreak cutting to be done exclusively in Low Range (L1–L3).
Capital Strategy: Analyse future procurement of next-generation estate tractors equipped with a Power Shuttle, Hydrostatic, or Powershift transmission to eliminate mechanical dry clutch wear entirely -- implications must be analysed
Root cause analysis

## Slide 6: Lack of thorough Daily Inspections & Terrain Impact
Evidence & Impact
  Asset Component Damage: Catastrophic, sudden failure of the engine top-end cylinder head assembly, detached/vibrating wiring harnesses, and a completely stripped starter motor gear.
  Slasher Fleet Wear: Continuous replacement cycles of 8 separate slasher Skid Runners between 2021 and 2025, culminating in a ZAR 26k replacement of the Slasher Gearbox in April 2025.
Likely Root Cause
  Missed Warnings: Major failures occurred because visible or audible operational warnings were consistently missed, ignored, or went unrecorded by operators.
  Terrain Abuse: Rough, undulating estate terrain and rocky firebreaks caused the slasher deck to continuously bottom out. Dragging the skid runners transferred high-impact shock loads directly up the PTO shaft, destroying the internal gearbox gears.
Daily Pre-Start Checklist: Enforce a mandatory, operator-signed morning inspection covering engine oil, cooling water levels, wire harness security, and ground fluid drips.
Clutch Housing Audit: Mandate a weekly technical check of the clutch housing weep hole.
Engineering Modification: Retrofit the estate slasher with heavy-duty trailing puncture-proof caster wheels to keep the skid runners 2–3 cm off the ground, eliminating ground-striking forces.
Root cause analysis

## Slide 7: Absence of an Economic Limit of Repair Policy
Establish an ELR Policy: Implement a strict, formalised Economic Limit of Repair framework to guide estate capital decisions
Asset-Level Cost Monitoring: Transition fleet financial oversight to a centralised ledger managed by the Finance Committee to track real-time utilisation alongside rolling repair thresholds.
The 30% Single Estimate Rule: Automatically red-flag, halt, and review any single repair quote that exceeds 30% of the tractor's current market value
The 50% Cumulative Rule: If the cumulative maintenance spend over any rolling 24-month window exceeds 50% of the asset's market value, stop repairs and route the tractor for immediate trade-in or disposal
Evidence and Impact:
  Financial Drain: Cumulative asset maintenance spend has exceeded ZAR 500k on a machine with an estimated market value of ZAR 200k
  Asset Management Failure: The tractor was permitted to continually drain estate capital because each maintenance invoice was evaluated as an isolated event rather than a compounding, cumulative total.
Likely Root Cause
  Policy Deficit: The estate lacked a formalised asset retention policy, financial cap structure, or lifecycle threshold to flag when a machine has structurally and economically expired
  Siloed Fleet Supervision: Management authorised major technical repairs as separate, isolated events due to an absence of an aggregated lifecycle expenditure tracker
Root cause analysis

## Slide 8: Proposed Next steps
Immediate Operational Control
(Weeks 1–2)
Print & Place Checklists: Bind and place the Daily Pre-Start Checklists directly inside the tractor cabin box.
[Draft checklists here: Checklists.docx]
Slasher Retrofit: Purchase and install heavy-duty, puncture-proof trailing caster wheels onto the Falcon slasher deck to establish the mandatory 2–3 cm ground clearance gap.
Establish Digital Influx: Generate the cloud folder upload QR code sticker and mount it directly onto the tractor dashboard for supervisor shift-end photo submissions.
Driver Accountability & Enforcement
(Weeks 3–4)
Practical Retraining: Conduct an on-site practical session for all estate drivers focusing strictly on Low-Range gear selection (L1–L3) and the "foot completely off the clutch" mandate. [Training Material here: Tractor Training.pptx]
Signed Accountability: Secure signed declarations from every operator confirming their understanding of the new speed modulation rules and the disciplinary consequences of clutch riding.
Launch Field Audits: Begin unannounced monthly Field Operator Verification Audits to actively police field compliance.
Strategic Capital Management
(Month 2 Onwards)
Formulate the ELR Policy: Present the formal Economic Limit of Repair framework to the estate board for official sign-off to codify the 30% single-estimate and 50% cumulative-expenditure boundaries.
Procurement Review: Initiate a market analysis for next-generation estate support vehicles featuring Hydrostatic or Power Shuttle transmissions to future-proof upcoming capital procurement cycles.